## Slide 1: TWf - Safety by Design & Engineering – Visual standards
Nick Boyle - September 2018

## Slide 2: Do we talk in a common language?

## Slide 3: Different Languages & Different Currencies
Roadworks - Chainage
Earthworks - Cut 4/Fill 5
Drainage Engineer - Network 3
Structures Engineer - Br 4
Site Engineer - Kgs and tonnes
TW Engineer - KN/m2
Architect - ?

## Slide 4: Once upon a time…..access to structures &shafts
Access Scaffold with Ladders

## Slide 5: Once upon a time…..access to structures &shafts
Access Scaffold with Ladders
And now….access towers with in- built steps

## Slide 6: So what has happened?
Crossrail C510 - 2015
Fatigue failure – 3 years in use
Action – regular inspection where extended usage
Crossrail C405 – 2018
Fatigue failure
3 to 4 times over capacity
Fracture in staircase
Overloaded – many years service
Some anecdotal evidence of other incidents

## Slide 7: Typical access stairs – a compact & standard – in the manual

## Slide 8: What are the Issues?
The brief – Lost in Space – multiple parties?
Ensuring fit for purpose – by all parties?
Temporary staircases – 3 years?
Regular Inspections?
In general - is it clear what the restrictions are on access scaffolds - at the point of use?

## Slide 9: Actions taken by Haki
Re-tested and re-rating standard stairs- 4kN/m2
Haki stair chart produced
Info shared with NASC – potential review of SG25:14 Access and Egress from Scaffolds via Ladders & Stair Towers?

## Slide 10: Final thoughts – At point of use for all access scaffolds - Are visual standards required for all?

## Slide 11: TWf - Follow on actions?
Access stair/scaffold failures - have there been other similar issues in industry? – other case studies from industry?
At point of use for all access scaffolds – visual standards are required?